## Slide 1
Phase Retrieval from the Short-Time Fourier Transform
Yonina Eldar
Technion – Israel Institute of Technology
Kishore Jaganathan and Babak Hassibi
Department of Electrical Engineering, Caltech
Optics Collaborators: Moti Segev and Oren Cohen

## Slide 2: Phase Retrieval: Recover a signal from its Fourier magnitude
Fourier + Absolute value
Arises in many fields: crystallography (Patterson 35), astronomy (Fienup 82), optical imaging (Millane 90), and more
Given an optical image illuminated by coherent light, in the far field we obtain the image’s Fourier transform
Optical devices measure the photon flux,
which is proportional to the magnitude
Phase retrieval can allow direct recovery
of the image

## Slide 3: Theory of Phase Retrieval
Difficult to analyze theoretically when recovery is possible
No uniqueness in 1D problems (Hofstetter 64)
Uniqueness in 2D if oversampled by factor 2 (Hayes 82)
No guarantee on stability
No known algorithms to achieve unique solution
Recovery from Fourier Measurements is Difficult!

## Slide 4: Progress on Phase Retrieval
Assume random measurements to develop theory (Candes et. al, Rauhut et. al, Gross et. al, Li et. al, Eldar et. al, Netrapalli et. al, Fannjiang et. al …)
Introduce prior to stabilize solution
  Support restriction (Fienup 82)
  Sparsity (Moravec et. al 07, Eldar et. al 11, Vetterli et. al 11, Shechtman et. al 11)
Add redundancy to Fourier measurements
  Random masks (Candes et. al 13, Bandeira et. al 13)
  Short-time Fourier transform (Nawab et. al 83, Eldar et. al 15,
  Jaganathan et. al 15)
  Small number of fixed masks (Jaganathan et. al 15)
Today

## Slide 5: Recovery From the STFT Magnitude
Easy to implement in optical settings
  FROG – measurements of short pulses (Trebino and Kane 91)
  Ptychography – measurement of optical images (Hoppe 69)
Also encountered in speech/audio processing (Griffin and Lim 84, Nawab et. al 83)
Almost all signals can be recovered as long as there is overlap between the segments
Almost all signals can be recovered using semidefinite relaxation
Efficient algorithms like GESPAR work very well in practice
L – step size
N – signal length
W – window length

## Slide 6: Talk Outline
Summary of phase retrieval results
Efficient algorithms
STFT in optics
Theoretical guarantees

## Slide 7: Analysis of Phase Retrieval
Analysis of Random Measurements:
  measurements needed for uniqueness
  (Balan, Casazza, Edidin o6, Bandira et. al 13)
random vector
How to solve objective function?
Stable Phase Retrieval (Eldar and Mendelson 14):
measurements needed for stability
) measurements needed for stability with sparse input
Solving provides stable solution

## Slide 8: Recovery via Semidefinite Relaxation
with ,
Phase retrieval can be written as
minimize rank (X)
subject to A(X) = b, X ≥ 0
SDP relaxation: replace by or by and apply reweighting
Advantages / Disadvantages
Convenient for proving recovery guarantees
Yields the true vector whp for Gaussian meas. (Candes et al. 12)
Recovers sparse vectors whp for Gaussian meas. (Candes et al. 12)
Computationally demanding
Difficult to generalize to other nonlinear problems
Candes, Eldar, Strohmer ,Voroninski 12

## Slide 9: Efficient Algorithms
General theory and algorithms for nonlinear sparse recovery
Derive necessary conditions for optimal solution
Use them to generate algorithms
Necessary Conditions:
L-stationarity Iterative Hard Thresholding
CW-minima Greedy Sparse Simplex (OMP)
Greedy sparse simplex can be shown to be more powerful than IHT
Beck and Eldar, 13
s.t.
Generalization of sparse recovery to the nonlinear setting!

## Slide 10: GESPAR: GrEedy Sparse PhAse Retrieval
Generalization of matching pursuit to phase retrieval
Local search method with update of support
For given support solution found via Damped Gauss Newton
Efficient and more accurate than current techniques
1. For a given support: minimizing objective over support by linearizing
the function around current support and solve for
    )
2. Find support by finding best swap: swap index with small value
with index with large value
Shechtman, Beck and Eldar, 13
determined by backtracking

## Slide 11: Performance Comparison
Each point = 100 signals
n=64
m=128

## Slide 12: Provable Efficient Algorithms for Phase Retrieval
  Wirtinger flow (gradient algorithm with special initialization) achieves the bound (Candes et. al 14,15)
  Wirtinger flow+thresholding requires measurements (Li et. al 15)
  All recovery results for random measurements (or random masks)
Moving to practice: Provable recovery from Fourier measurements?
Recent overview:
Y. Shechtman, Y. C. Eldar, O. Cohen,
H. N. Chapman, J. Miao, and M. Segev,
“Phase retrieval with application to optical imaging,”
SP magazine 2015

## Slide 13: Frequency-Resolved Optical Gating (FROG)
Trebino and Kane 91
L – step size
N – signal length
W – window length
Method for measuring ultrashort laser pulses
The pulse gates itself in a nonlinear medium and is then spectrally resolved
In XFROG a reference pulse is used for gating
leading to STFT-magnitude measurements:

## Slide 14: Ptychography
Hoppe 69
Plane wave
Scanning
For all positions () record diffraction
pattern
Method for optical imaging with X-rays
Records multiple diffraction patterns as a function of sample positions
Mathematically this is equivalent to recording the STFT

## Slide 15: Current and New Results
Existing results:
Fienup-type algorithms – iterate between constraints in time and constraints in frequency
    Griffin-Lim (Griffin and Lim 84)
    XFROG (Kane 08)
No general conditions for unique solution
No general proofs of recovery
Our contribution:
Uniqueness results from STFT measurements
Guaranteed recovery using semidefinite relaxation
Efficient algorithm: Adaption of GESPAR
Extension of results to masked measurements

## Slide 16: Theoretical Guarantees
Theorem (Eldar, Sidorenko, Mixon et. al 15)
The STFT magnitude with L=1 uniquely determines any x[n] that is everywhere
nonzero (up to a global phase factor) if:
The length-N DTFT of is nonzero
N and W-1 are coprime
Theorem (Jaganathan, Eldar and Hassibi 15)
The STFT magnitude uniquely determines almost any x[n] that is everywhere
nonzero (up to a global phase factor) if:
The window g[n] is nonzero
2.
Uniqueness condition for L=1 and all signals:
Uniqueness condition for general overlap and almost all signals:
Strong uniqueness for 1D signals and Fourier measurements (without sparsity)

## Slide 17: Recovery From STFT via SDP
Theorem (Jaganathan, Eldar and Hassibi 15)
SDP relaxation uniquely recovers any x[n] that is everywhere nonzero from the
STFT magnitude with L=1 (up to a global phase factor) if
In practice SDP relaxation seems to work as
long as (at least 50% overlap)
Strong phase transition at L=W/2
Probability of Success for N=32 for different
L and W
Can prove the result assuming the first W/2 values of x[n] are known
L=W/2
L
W

## Slide 18: GESPAR for STFT Recovery
W=16, N=64 varying L
L=2,4,8,16 (no overlap)
Eldar, Sidorenko et. al 15
PS GESPAR uses oversampled FT with the same number of measurements as STFT

## Slide 19: Recovery from Lowpass Data
Original
Blurred
Reconstruction
Line out
Orig.
Blurr.
Rec.
Sidorenko et al

## Slide 20: Coded Diffraction Patterns
Candes, Li and Soltanolkotabi 13
Modulate the signals with masks before measuring
Assume an admissible mask d[k] for which
Using masks the signal can be recovered
Gross et. al improved to
Difficulty: random masks, large constants

## Slide 21: Efficient Masks
2 deterministic masks each with 2N measurements suffice!
To recover all signals x[n] we can use specific masks which also guarantee stable recovery via SDP
Theorem (Jaganathan, Eldar and Hassibi 15)

## Slide 22: Efficient Masks
Idea can be extended to allow for 5 masks, and each one measured with only N measurements
Theorem (Jaganathan, Eldar and Hassibi 15)
Any can be recovered in a robust fashion from the two
previous masks using a semidefinite relaxation

## Slide 23
STFT provides an effective way to measure in the Fourier domain
Provides better recovery for the same number of measurements
Provable recovery guarantees
Efficient methods in practice
Deterministic robust masks can be constructed that are very efficient
Future work: complete SDP relaxation analysis
Practical Method for Fourier Phase Retrieval
Conclusion

## Slide 24: Thank you!